Western Carolina University

2006 -2007

Strategic Energy Plan

Submitted October 1, 2007

Energy Management Office

Facilities Management

Contents

- Mission Statement

- Executive Summary

- Consumption Data

- Accomplishments and Goals

  - Energy Data Management

  - Energy Supply Management

  - Energy Use in Facilities

  - Equipment Efficiency

  - Organizational Integration

- Energy Mandate

1.  Mission Statement

To develop smart energy solutions in all aspects of our institution and create a comprehensive approach for leading the Western Carolina University community towards a sustainable future.

2.  Executive Summary

During 2006-2007 Western Carolina University continued its efforts to progress in the area of waste reduction, lowering utility costs and reducing our carbon footprint.  One of our focuses has been on the acquisition of energy management software, Itron Enterprise Energy Management (EEM) Suite.  This software will allow us to perform many functions including bill analysis, meter data analysis, and forecasting to assist us with achieving efficiencies in energy conservation, usage forecasting, operations and billing practices.  It combines bill data and meter data with a utility-grade rate engine and rate library, which automates the process of cost allocation, bill validation, budget creation and tracking.  Through accurate forecasting of regular energy needs, as well as peak load potential, EEM Suite will help us avoid risk and high energy cost by proactively managing operations and energy procurement.  EEM Suite will also track greenhouse gas emissions and benchmark facilities against external organizations through integration with the ENERGY STAR® National Energy Rating System, which will improve our ability to implement and manage resource conservation programs.

We launched a campus wide energy conservation program called WHEE Save.  The purpose of this program is to educate faculty, staff and students about energy consumption and how it affects the economy, environment and our overall footprint on the Earth.  Our goals are to raise awareness about the ecological and economical benefits of conserving energy, teach methods on how to reduce energy consumption on campus, have a positive impact on long term energy consumption habits of our university community and lower overall energy consumption.  We have a comprehensive approach for this program including informational materials, lectures, involvement with faculty, staff and student groups.  It has gained momentum campus-wide and become recognized by a large percent of our campus population.  The GHG emissions reporting feature in EEM Suite will help us further these efforts next year.

We are also planning a project to install utility meters on campus buildings.  This will begin with seven of our largest appropriated funded buildings (Hunter Library, HF Robinson, Ramsey Activity Center, Fine and Performing Arts Center, Center for Applied Technology, McKee and Stillwell) during the upcoming fiscal year.  We will be measuring electricity, domestic water and steam (condensate).  The new meters will integrate into our campus network and send information back to EEM Suite.  We will continue to develop meter projects until all campus buildings are incorporated into the new system.  This will provide us with baseline data to enable us to initiate performance contracting in the near future.

This year we are planning our first building on our new west campus.  The Health & Gerontological Science complex, funded by state legislation as a capital bond project, will be a 138,000 sq/ft flagship facility for the new section of campus.  We plan to achieve Silver LEED certification for this project and want to create this as a building standard for all new construction at Western Carolina University.

Table 1 below summarizes our energy usage over the past 5 years.  Overall, our energy performance has continued to improve.  Total utility cost and energy consumption increased as expected, primarily due to rising fuel costs and an increase in total gross square footage (GSF-See Table 2).    However, energy cost per square foot and per MM BTU decreased significantly during the past year.

Table 1:  WCU Energy Performance, 2002-to-2007

| YEAR | TOTAL UTILITY COST $ | $/MM BTU | $ / GSF | BTU / SQ.FT. | % CHANGE, BTU/SQ FT (cumulative) |
| --- | --- | --- | --- | --- | --- |
| 2002-2003 | $3,075,813 | $6.35 | $1.14 | 178,764 | 00 |
| 2003-2004 | $3,300,828 | $9.18 | $1.26 | 136,616 | -24% |
| 2004-2005 | $3,798,840 | $9.59 | $1.25 | 129,989 | -27% |
| 2005-2006 | $4,288,287 | $12.77 | $1.45 | 113,548 | -36% |
| 2006-2007 | $4,404,131 | $11.66 | $1.43 | 123,042 | -31% |

This improvement is primarily a result of retiring old equipment, installing new equipment with higher operating efficiencies, building improvements and successful educational programs for faculty, staff and students.  Since the beginning of the Utility Savings Initiative in 2003, the combined benefits of these items reflect a reduction of energy consumption per gross square foot of 31%.

3.  Consumption Data (See Table 2 – attached)

4.  Accomplishments and Goals

A.  Energy Data Management

| Past Year Activities | Measurement | Savings Actual or Calculated | Cost | Funding Source |
| --- | --- | --- | --- | --- |
| Review of Energy Usage for Fee Supported Buildings | Monthly | No changes | 20 hours per month | FM Operating Budget |
| Purchased Energy Management Software – Itron Enterprise Energy Management (EEM) Suite | Bill Analyst (bill processing & validation, bill & budget tracking), Meter Data Analyst (use & rate analysis, baseline performance, bill/meter reconciliation, alarm management, rate modeler), Forecasting & Meter Data Validation | Will see impact next Fiscal Year | $125,250 | Year End Monies |
| Purchased Server for EEM Suite | None | None | $6,541 | FM Operating Budget |
| Programmed Building Automation System (BAS) to record outside weather data | Continuous. Includes average temperature, high/low temperature, heating & cooling degree days | To be determined | 8 hours | FM Operating Budget |
| Programmed BAS to track BTU output of Chilled and Hot Water Systems in Central Drive Hall | Continuous & Monthly Total | To be determined | 2 hours | FM Operating Budget |
| Migrated BAS into single web sever based front end. Simplifies user operation and is accessible from any computer on campus network | Continuous | Enhanced functionality and usability | 160 hours (ongoing as needed) | FM Operating Budget |
| Installed new condensate meter at HF Robinson and integrated into BAS | Continuous | To be determined | 15 hours $250 | FM Operating Budget |
| Installed new condensate meter at Leatherwood Hall and integrated into BAS | Continuous | To be determined | 15 hours $250 | FM Operating Budget |
| Repaired original installation of condensate meter at CDH in order to achieve accurate reading | Continuous | To be determined | 8 hours | FM Operating Budget |
| Created program to track equipment run time on Air Handler Units. Information is used by Preventative Maintenance Coordinator to schedule filter changes and other PM | Continuous | To be determined | 40 hours | FM Operating Budget |
| Planned Activities 2007-2008 | Measurement | Savings Estimated | Cost | Funding Source |
| Installation of meters at Ramsey Activity Center, Hunter Library, Fine & Performing Arts, Stillwell, HF Robinson, McKee, Center for Applied Technology | Interval readings for electric, water, steam condensate | Will see impact next Fiscal Year | $175,000 | R & R |
| All new buildings will have proper meters that integrate into Itron EEM Suite. New construction includes: Student Recreation Center, Dining Facility & Residence Hall | Interval readings for electric, water, steam condensate | Will see impact next Fiscal Year | To be determined | Capital |
| Launch BAS Phase II Project for all buildings with outdated and/or lacking DDC controls | Continuous | Will see impact next Fiscal Year | To be determined | TBD |

B.  Energy Supply Management

| Past Year Activities | Measurement | Savings Actual or Calculated | Cost | Funding Source |
| --- | --- | --- | --- | --- |
| Revised electric rates to include demand for all fee-supported auxiliary organizations (Residential Living, Dining Services, Health Services, Bookstore, University Center & Old Student Union) | Monthly meter readings | Equitable distribution of cost | 3 hours | FM Operating Budget |
| Revised water rates to reflect actual cost of production for fee-supported auxiliary organizations | Monthly meter readings | Equitable distribution of cost | 3 hours | FM Operating Budget |
| Review natural gas rates for steam plant consumption. Incurred savings thru matching fuel costs | Monthly | $132,774.81 | 2 hours | Salary |
| Planned Activities 2007-2008 | Measurement | Savings Estimated | Cost | Funding Source |
| Utility Billing review | Monthly | To be determined | 12 hours | FM Operating Budget |
| Utility Rate review | Monthly | To be determined | 6 hours | FM Operating Budget |
| Utilize Itron EEM Suite to lower peak demand usage | Monthly | To be determined | 15 hours | FM Operating Budget |
| Investigate renewable energy technologies for energy supply. Solar hot water heating seems most applicable | On-going | To be determined | To be determined | FM Operating Budget |

C.  Energy Use in Facilities

| Past Year Activities | Measurement | Savings Actual or Calculated | Cost | Funding Source |
| --- | --- | --- | --- | --- |
| Install T-8 electronic ballast for lighting when replacing bad T-12 and magnetic ballasts | As needed | To be determined | 10 Ballasts per week | FM Operating Budget |
| Install CFL bulbs to replace all bad incandescent bulbs | As needed | To be determined | 218 units per year at $5.77 each $1257.86 total | FM Operating Budget |
| Replaced single-paned windows in Belk Building with double paned | Monthly | To be determined | $678,180 | R & R |
| Replaced failed built-up roofs on McKee (reflective white membrane), Breese Gym & Hunter Library (reflective white membrane). New system has insulated panels with membrane roof | Monthly | To be determined | $219,148 (McKee), $184,440 (Breese Gym) $1,167,449 (Hunter) | R & R |
| Continued to monitor campus wide heating and cooling temperature set points based on state mandate requirements and University Policy #4 | Daily | To be determined | 4 hours per week | FM Operating Budget |
| Established BAS Protocol for troubleshooting, temperature set point exceptions and collecting building schedules | As needed | To be determined | 20 hours Initially/4 hours per month | FM Operating Budget |
| Request activity and operation schedule from designated building coordinators at the beginning of every term for all buildings. Utilized to set HVAC equipment schedules accordingly. Special events are sent to Energy Management weekly, monthly as needed basis | As needed | To be determined | 10 hours per month | FM Operating Budget |
| Purchased HOBO (temp/humidity) Data Loggers and BoxCar Pro 4.3 software to assist troubleshooting HVAC issues | As needed | To be determined | $609.00 | FM Operating Budget |
| Planned Activities 2007-2008 | Measurement | Savings Estimated | Cost | Funding Source |
| Continue to send out campus wide energy announcements | As needed | To be determined | As needed | FM Operating Budget |
| Notified campus and enforced 78 temperature set point mandate from NC Governor’s office during peak demand heat wave period in August. | As needed | To be determined | 20 hours | FM Operating Budget |
| Notified campus of Exceptional Drought Conditions on 8/27/07 as announced by NC Governor’s Office. Included water conservation tips and requested cooperation to reduce water usage from campus community. Ceased washing all motor pool and motor fleet management vehicles until further notice from state. | As needed | To be determined | 1 hour | FM Operating Budget |
| Continue to request building schedules at the beginning of every semester | As needed | To be determined | 10 hours per month | FM Operating Budget |
| New Health & Gerontological Building to be Silver LEED Certified | On-Going | To be determined | 48 M | Capital |
| Continue to upgrade lighting to T-8 and CFLs | As needed | To be determined | To be determined | FM Operating Budget |
| Replace single pane windows with double pane/low-e at Facilities Management Building | Monthly | To be determined | To be determined | R & R |
| Replace roof on University Bookstore (reflective white membrane) and Moore Building New system has insulated panels with membrane roof | Monthly | To be determined | $383,745 (Moore), TBD (Bookstore) | Auxiliary Services, R & R |

D.  Equipment Efficiency

| Past Year Activities | Measurement | Savings Actual or Calculated | Cost | Funding Source |
| --- | --- | --- | --- | --- |
| Replaced faulty chilled water valve at Hinds University Center | Daily | To be determined | $248.33 6 hours | FM Operating Budget |
| Programmed economizer sequence into AHU-1 at Breese Gymnasium | As-needed | To be determined | 4 hours | FM Operating Budget |
| Restored original sequence of operation to air make-up units at Central Hall Drive | As-needed | To be determined | 2 hours | FM Operating Budget |
| Modified sequence and added economizer function into AHUs at Center for Applied Tech Building | As-needed | To be determined | 8 hours | FM Operating Budget |
| Programmed economizer sequences into 3 AHUs at Killian Annex Building | As-needed | To be determined | 8 hours | FM Operating Budget |
| Replaced 4 failed/aging hot water heaters with more efficient instant hot water heater in Residence Halls | As-needed | To be determined | $73,286 | Residential Living |
| Replaced obsolete boiler at Ramsey Center with 2 new high efficiency electric boilers integrated into BAS | Monthly | To be determined | $264,197 | R & R |
| Investigated feasibility of Performance Contracting | On-Going | To be determined | On-going | FM Operating Budget |
| Stillwell Renovation Phase I – upgraded lighting, HVAC replacement, improved insulation and building envelope | To be determined | To be determined | $12 M | Bond |
| Replaced Chiller and chilled water loop that supplies Stillwell, Hoey, McKee and Hunter Library | Monthly | To be determined | $600,000 | R & R |
| Perform steam trap survey to assess system issues | Annually | To be determined | $1,213.90 61 hours | FM Operating Budget |
| Repaired leaky steam lines during steam shut-down in May | Annually | To be determined | $18,002.35 37231.76 hours | FM Operating Budget |
| Steam line infrastructure replacement on lower campus | Monthly | Estimated Loss $100,000 condensate/year | $742,934 | R & R |
| Planned Activities 2007-2008 | Measurement | Savings Estimated | Cost | Funding Source |
| Replace 2 aging hot water heaters with more efficient instant hot water heater in Residence Halls | As-needed | To be determined | To be determined | Residential Living |
| Investigated feasibility of Performance Contracting | On-Going | To be determined | On-Going | FM Operating Budget |
| Perform steam trap survey to assess system issues | Annually | To be determined | To be determined | FM Operating Budget |
| Repaired leaky steam lines during steam shut-down in May | Monthly | To be determined | To be determined | FM Operating Budget |
| Forsyth Renovation upgrading HVAC Controls and adding economizers | To be determined | To be determined | 3 M | Bond |
| Stillwell Renovation Phase II - upgraded lighting, HVAC replacement, improved insulation and building envelope | To be determined | To be determined | $12 M | Bond |
| Construct Central Chiller Plant for new Dining Facility and Residence Hall | To be determined | To be determined | To be determined | Privatized |

E.  Organizational Integration

| Past Year Activities | Measurement | Savings Actual or Calculated | Cost | Funding Source |
| --- | --- | --- | --- | --- |
| Launched WHEE Save – campus wide energy conservation awareness and education program. Includes energy reports in publications, emails, distribution of informational materials (brochures, posters, stickers), new employee orientation & one-on-one meetings | On-going | To be determined | 25 Hours per month | FM Operating Budget |
| Member of WCU Wellness Council as Energy/Sustainability Initiatives representative | On-going | To be determined | 2 Hours per month | FM Operating Budget |
| Member of Faculty Learning Community for Campus Sustainability Initiatives as Energy Management liaison for WCU | On-going | To be determined | 2 Hours per month | Volunteer time |
| Shifted Energy Management Specialist position from HVAC Shop to Energy Management | On-going | To be determined | 4 Hours | FM Operating Budget |
| Continued regular discussion of energy savings objectives in planning stages of all bond projects | On-going | To be determined | On-going | FM Operating Budget |
| Updated Strategic Energy Plan | Once a year | To be determined | 40 Hours | FM Operating Budget |
| Involved in Student Programs – Advisor for Eco CATS Student Club, advisor for Clean Energy Initiative & advise collaboration with other student clubs | On-going | To be determined | 20 Hours per month | Volunteer Time |
| Planned Activities 2007-2008 | Measurement | Savings Estimated | Cost | Funding Source |
| Continue to emphasize energy conservation and achieving s668 energy efficient standards in state buildings during design and construction of new buildings | On-going | To be determined | On-going | FM Operating Budget |
| Continue to promote WHEE Save for faculty, staff & students | Quarterly | To be determined | 25 hours | FM Operating Budget |
| Presented display table at Southern Energy and Environmental Expo (SEE Expo) Asheville, NC | Annually | To be determined | 40 hours | FM Operating Budget |
| Presented display table at WCU Employee Appreciation Day | Annually | To be determined | 3 Hours | FM Operating Budget |
| Collaborate with WCU Faculty for Energy Management lectures for class instruction and assist with student projects related to energy | On-going | To be determined | On-going | FM Operating Budget |
| Continue to stay involved in variety of student programs and clubs | Weekly | To be determined | On-going | Volunteer Time |
| Chancellor Bardo to sign the President’s Climate Commitment | On-going | To be determined | On-going | FM Operating Budget |

F.  Water Management

| Past Year Activities | Measurement | Savings Actual or Calculated | Cost | Funding Source |
| --- | --- | --- | --- | --- |
| Repaired major water leak at the Greek Village (200,000 to 300,000 gallons per month since occupancy in August 2003). Leak created during construction | Monthly | $800,000/month | $10,000 | FM Operating Budget |
| Replace shower heads (5 per week), faucets 2.2 gpm aerators and flush valves (15 per week) with low flow fixtures | As needed | To be determined | 30% Plumbing Shop labor time per week | FM Operating Budget |
| Repair leaks when observed or reported to Facilities Management | As needed | To be determined | 60% Plumbing Shop labor time per week | FM Operating Budget |
| Planned Activities 2007-2008 | Measurement | Savings Estimated | Cost | Funding Source |
| Continue to repair leaks and install low flow shower heads, flush valves | As needed | To be determined | 90% Plumbing Shop Labor per week | FM Operating Budget |

Energy Declaration

I have read the Strategic Energy and Water Plan for Western Carolina University.

The plan, as presented, supports the reduction required in Senate Bill 668.

Implemented this ____ day of __________________, 2007.

_______________________________

Dr. John Bardo

Chancellor

_______________________________

Mr. Chuck Wooten

Chief Financial Officer

_______________________________

Joe Walker, III, P.E.

Associate Vice Chancellor for Facilities Management

_______________________________

Lauren R. Bishop

Energy Manager